## Slide 1
An event-based IEEE 802.11ax WLANs Simulator
Sergio Barrachina-Muñoz, Francesc Wilhelmi

## Slide 2
Introduction

## Slide 3: Introduction to the simulator
Open source, available at https://github.com/wn-upf/Komondor
Based on COST
  Implementation of IEEE 802.11ax novel functionalities
  High-density scenarios
  Prepared to handle intelligent agents
Technical report at https://github.com/wn-upf/Komondor/blob/master/Documentation/Technical%20Report/LaTeX%20files/komondor_technical_report.pdf

## Slide 4: COST
CompC++ library that allows generating discrete event simulations
Main website: http://www.ita.cs.rpi.edu/cost.html
Nodes are represented by components
Message exchange between nodes through outport/inport connections
Timers for triggering events (e.g., end of transmission)
Fig. 1: Component in COST

## Slide 5: Overview
Fig. 2: Komondor flowchart

## Slide 6
IEEE 802.11 Features

## Slide 7: Channel Access
Distributed Coordination Function (DCF): Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA) with Binary Exponential Backoff (BEB)
  Slotted vs Continuous Backoff (BO)
  Uniform vs Exponential distributions for BO calculation
Capture Effect (CE): stronger-first approach
Fig. 3: Capture Effect approach

## Slide 8: RTS/CTS
Ready-To-Send/Clear-To-Send (RTS/CTS) is mandatory
Virtual carrier sensing is done
Fig. 4: RTS/CTS utilization example

## Slide 9: Channel Bonding
Several implemented policies:
  Only Primary (OP)
  Static Channel Bonding (SCB):
  Always-max (AM)
  Probabilistic uniform (PU)
Fig. 6: CSMA/CA temporal evolution under the utilization of AM
Fig. 5: Channel access when AM is applied

## Slide 10: Packet Aggregation
Concatenation of N MPDUs to be sent over the same packet transmission
Acknowledged by a Block-ACK (BACK)
Fig. 7: Packet aggregation for a single transmission

## Slide 11
Design Principles

## Slide 12: Architecture based on states
The IEEE 802.11ax-based Simulator considers several states to capture the behavior of nodes
  Sensing
  NAV
  Transmitting an RTS or a CTS
  Receiving an RTS or a CTS
  Transmitting DATA
  Receiving DATA
  …

## Slide 13: Channel Modeling
Several Path-loss models (easy to add new ones):
  Free Space Path Loss (FSPL)
  Okumura-Hata model
  Generic indoor model
  IEEE 802.11ax residential scenario model
Different adjacent channel interference models:
  No interference
  Limited interference: only adjacent channels leak power
  Total interference: all the channels leak power (20 dB per channel)
Assumption: the incoming power in a given receiver is assumed to be the same during the entire transmission

## Slide 14: Traffic Modeling
Three implemented models for traffic generation:
Fig. 8: Traffic generation models

## Slide 15: Link Modeling
IEEE 802.11ax MCS are used
Tbl. 1: IEEE 802.11ax MCS table
Assumption: The MCS is computed at the beginning of the simulation, based on the power received from the transmitter

## Slide 16: Collisions Modeling
Packet losses occur if:
  The destination is already transmitting
  The signal strength is not strong enough (Prx < CCA)
  The CE is not accomplished due to interference
  The destination is already receiving a packet and the CE condition is still accomplished for the first transmission
  The destination is in NAV
  Backoff collisions

## Slide 17
Validations

## Slide 18: System parameters
Tbl. 2: IEEE 802.11ax PHY & MAC parameters
IEEE 802.11ax parameters are considered
  Channel access
  Frames length
  Channelization
  …

## Slide 19: Basic Operation
Scenario
Packet aggregation (N = 64) |  | 
Komondor | ns3 | Bianchi
91.45 Mbps | 90.71 Mbps | 91.44 Mbps
Single packet (N = 1) |  | 
Komondor | ns3 | Bianchi
26.87 Mbps | 25.28 Mbps | 26.87 Mbps
Results
 | Position AP (m) | Position STA (m) | Channel | Transmit power (dBm) | CCA (dBm)
AP | [2,2,0] | - | 1 | 20 | -68
STA A | - | [0,0,0] | 1 | 20 | -68
Tbl. 3: Configuration Scenario 1
Tbl. 4: Results Scenario 1
Fig. 9: Scenario 1

## Slide 20: Two STAs
Scenario
Packet aggregation (N = 64) |  | 
Komondor | ns3 | Bianchi
91.45 Mbps | 90.71 Mbps | 91.44 Mbps
Single packet (N = 1) |  | 
Komondor | ns3 | Bianchi
26.87 Mbps | 25.28 Mbps | 26.87 Mbps
 | Position AP (m) | Position STA (m) | Channel | Transmit power (dBm) | CCA (dBm)
AP | [2,2,0] | - | 1 | 20 | -68
STA A | - | [0,0,0] | 1 | 20 | -68
STA B | - | [4,4,0] | 1 | 20 | -68
Results
Tbl. 5: Configuration Scenario 2
Tbl. 6: Results Scenario 2
Fig. 9: Scenario 2

## Slide 21: Dynamic Channel Bonding
Scenarios
Results
More information in Barrachina-Munoz, S., Wilhelmi, F., & Bellalta, B. (2018). Performance Analysis of Dynamic Channel Bonding in Spatially Distributed High Density WLANs. arXiv preprint arXiv:1801.00594.
Fig. 10: Scenarios for DCB validation
Fig. 11: Results DCB validation

## Slide 22
Intelligent Agents

## Slide 23: Some remarks
Agents are introduced to modify the configuration of simulated WLANs in order to maximize a certain performance metric (local or globally)
Each agent is associated to an AP, so that all the information is shared between these two type of entities (we assume that the agent is located in the AP)
Communication between agents is not implemented yet, but future developments contemplate centralized approaches
  Agents share information with a central entity, which takes decisions
  Adaptive delay for such a communication

## Slide 24: Overview
Legacy
Legacy
Decentralized Learning
Decentralized Learning
Centralized Learning
Centralized Learning
Centralized Learning
Central Entity

## Slide 25: AP-Agent communication
t
t
ouportRequestInformationToAp()
inportReceivingRequestFromAgent()
ouportAnswerToAgent()
inportReceivingInformationFromAp()
ouportSendConfigurationToAp()
inportReceiveConfigurationFromAgent()
Function
Outport
Inport
Node :: GenerateConfiguration()
Node :: GeneratePerformanceReport()
Agent:: RequestInformationtoAp()
Agent:: ComputeNewConfiguration()
Agent:: SendNewConfigurationToAp()
Agent:: GenerateRewardSelectedArm()
Node :: ApplyNewConfiguration()

## Slide 26: Agent-oriented functionalities at the AP
Wait for agent requests → inportReceivingRequestFromAgent() ouportRequestInformationToAp()
Encapsulate important information regarding the current configuration (transmit power, CCA, MCS…) and the offered performance (packets sent, packets lost, collisions by hidden node…) → GenerateConfiguration() GeneratePerformanceReport()
Send information to the Agent → ouportAnswerToAgent()
Wait for the new configuration granted by the Agent → inportReceiveConfigurationFromAgent()
Apply changes and broadcast new configuration to STAs → ApplyNewConfiguration()

## Slide 27: Agent functionalities
Generate and send requests for APs periodically → RequestInformationtoAp() ouportRequestInformationToAp()
Wait for the requested information → inportReceivingInformationFromAp()
Generate a reward according to the current configuration and performance in the AP → GenerateRewardSelectedArm()
Draw a new configuration according to updated rewards → ComputeNewConfiguration()
Send the new configuration to the AP → SendNewConfigurationToAp()
ouportSendConfigurationToAp()

## Slide 28: Centralized Learning - Remarks
In order to perform centralized learning, we have added a central entity that controls the operations done by agents
The central entity works on the top of the Agent-AP operation
It is important to remark that agents can be freely assigned to the central entity, so that we can support hybrid scenarios with
  Legacy APs
  Agent-embedded APs
  Centralized agent-embedded APs
Each agent communicates to the centralized entity in a synchronized manner

## Slide 29: Agent-Central Entity (CC) communication
t
t
ouportRequestInformationToAgent()
inportReceivingRequestFromController()
ouportAnswerToController()
inportReceivingInformationFromAgent()
ouportSendConfigurationToAgent()
inportReceiveConfigurationFromController()
Function
Outport
Inport
CentralController :: RequestInformationtoAgent()
CentralController :: ComputeNewConfiguration()
CentralController :: SendNewConfigurationToAgent()
CentralController CentralController :: GenerateRewardSelectedArm()
Start request of information to the AP
Forward the new configuration to the AP

## Slide 30: Agent-embedded Architecture
Central Entity
Agent
Access Point
Current Operation
MAC
PHY
Performance Report Generation
ConfigurationReport Generation
Communication with AP
Communication with CE
Algorithm
Process Input
Update configuration
Update Configuration
Receive new configuration from CE
Generate new configuration
Algorithm
Process Input
Generate Global Configuration
Retrieve information from agents